## Slide 1
King Faisal University
College of Computer Sciences and
Information Technology (CCSIT)
Submitted to: Engr. Amani Bayer.
CE 313 Computer Organization and Architecture

## Slide 2
Section | ID | Name of Group members
81 | 222427138 | Atekah Hussain Aljafar
81 | 222411640 | Fatimah Nasser Albesher
81 | 222412119 | Fatimah Hussain Alabdellah

## Slide 3
Introduction

## Slide 4: Introduction
This project focuses on implementing basic data processing tasks using assembly language. The program processes set of numbers stored in memory, performing operations such as separating the even numbers, averaging, and sorting.
The project also focuses on structured programming principles by leveraging subroutines for each specific task and implementing stack operations to manage subroutine calls and local data.

## Slide 5
Problem Statement

## Slide 6: Problem Statement
Problem Description:
Write a program in Assembly language that reads the numbers
from memory
(num1: dw 16,17,18,19,20,21,22,23,24,25,26,27,28,29,30,31,32)
and perform following operations on them:

## Slide 7: Problem Statement
Separate the even numbers and store the result (even numbers) in consecutive memory locations in an array (dw) named 'even’.
Find the average of numbers from even array and store in array name avg : dw 0

## Slide 8: Problem Statement
Sort the numbers from given array (num2: dw 0, 1, 2, 3, 4, 5, 6, 7,8,9,10) in descending order . Store the result in consecutive memory locations in an array (dw) named sort.
There should be separate subroutines for each mentioned task like even, average, sort. Also implement stack concept within each subroutines.

## Slide 9
Project Implementation with output screenshots

## Slide 10: Project Implementation with output screenshots
[ORG 0x2000]
jmp start
num1: dw 16,17,18,19,20,21,22,23,24,25,26,27,28,29,30,31,32
even: dw 0, 0, 0, 0, 0, 0, 0, 0, 0
sumEven: dw 0
avg: dw 0
num2: dw 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, 10
sort: dw 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, 0

## Slide 11: Project Implementation with output screenshots
loopeven:
mov ax,[bx]
and ax,1
jnz skip
mov ax,[bx]
mov [bp], ax
add bp, 2
EvenNum:
mov bx, num1
mov bp, even
mov cx,17

## Slide 12: Project Implementation with output screenshots
sum:
mov ax, 0
mov cx, 9
sum_loop:
add ax, [bx]
add bx, 2
loop sum_loop
ret
skip:
add bx,2
loop loopeven
ret

## Slide 13: Project Implementation with output screenshots
DecOrder:
push cx
push bx
mov di, sort
average:
mov cx, 9
mov bx, ax
xor dx, dx
div cx
ret

## Slide 14: Project Implementation with output screenshots
ShiftRight:
mov [di + 2], dx
add di, 2
jmp FindPosition
FindPosition:
cmp di, sort + 20
jge InsertValue
mov dx, [di]
cmp dx, ax
jl ShiftRight
jmp InsertValue

## Slide 15: Project Implementation with output screenshots
start:
call EvenNum
mov bx, even
call sum
mov [sumEven], ax
call average
mov [avg], ax
InsertValue:
mov [di], ax
pop bx
pop cx
ret

## Slide 16: Project Implementation with output screenshots
SortLoop:
mov ax, [bx]
call DecOrder
sub bx, 2
loop SortLoop
mov ax, 0x4c00
int 0x21
mov bx, num2 + 20
mov ax, [bx]
mov [sort], ax
sub bx, 2
mov cx, 10

## Slide 17: Project Implementation with output screenshots
Even |  | 
dec | hex | 
16 |  | [even]
18 |  | [even+2]
20 |  | [even+4]
22 |  | [even+6]
24 |  | [even+8]

## Slide 18: Project Implementation with output screenshots
Even |  | 
dec | hex | 
26 |  | [even+10]
28 |  | [even+12]
30 |  | [even+14]
32 |  | [even+16]

## Slide 19: Project Implementation with output screenshots
sumEven |  | 
dsec | hex | 
216 |  | [sumEven]
avg |  | 
dsec | hex | 
24 |  | [avg]

## Slide 20: Project Implementation with output screenshots
sort |  | 
dec | hex | 
10 |  | [sort]
9 |  | [sort+2]
8 |  | [sort+4]
7 |  | [sort+6]
6 |  | [sort+8]

## Slide 21: Project Implementation with output screenshots
sort |  | 
dec | hex | 
5 |  | [sort+10]
4 |  | [sort+12]
3 |  | [sort+14]
2 |  | [sort+16]

## Slide 22: Project Implementation with output screenshots
sort |  | 
dec | hex | 
1 |  | [sort+18]
0 |  | [sort+20]

## Slide 23
Conclusion

## Slide 24: Conclusion
The Assembly language program effectively demonstrates structured data manipulation through three tasks: separating even numbers, calculating their average, and sorting an array in descending order.
By using distinct subroutines for each operation, the program enhances modularity and readability.
The implementation of stack management highlights efficient resource handling in Assembly language. Overall, this program serves as a valuable educational tool, illustrating key principles of low-level programming, including data manipulation and memory management, while reinforcing the importance of structured programming practices.

## Slide 25: Thanks!